## Slide 1: MindCore: Spike-Driven Programmable Accelerator for On-device Neuromorphic Computing
Hawon Park, Si Yong Lee, Ryangjin Lee, Yoora Kim, Yoon Seok Yang
INTRODUCTION
The rapid expansion of artificial intelligence has intensified the need for energy-efficient edge computing. Traditional deep neural networks achieve high accuracy but are computationally and power intensive, limiting deployment on low-power devices.
Spiking Neural Networks (SNNs) offer a biologically inspired alternative through event-driven processing, enabling low-latency and power-efficient computation. However, conventional processors are poorly suited to spike-based operations, creating a gap between algorithmic potential and practical hardware realization.
To overcome this, we present MindCore, a spike-driven accelerator tailored for on-device SNN inference. MindCore integrates an optimized RISC-based controller with programmable neuron and synapse cores, supporting diverse neuromorphic models. Its custom instruction set enables efficient spike-vector operations, SIMD accumulation, and multi-precision arithmetic, while a hardware-level compression scheme reduces spike/event data volume by over 98%, minimizing memory and bandwidth demand.
Implemented on a Xilinx ZCU104 FPGA, MindCore provides a complete software stack and demonstrates significant power savings in event-based vision and biomedical inference tasks.
MindCore DESIGN
MindCore is an event-driven neuromorphic accelerator built on a RISC-based architecture optimized for spike-domain computation. It integrates a dedicated Spike Processing Unit (SPU) that performs spike-based arithmetic and communication with minimal control overhead.
RISC Controller & Spike Processing Unit (SPU)
Streamlined RISC pipeline manages instruction scheduling, memory, and spike data.
Integrated Spiking Logic Unit (SLU) executes custom spike instructions — bitwise logic, spike counting, and SIMD accumulation — in a single clock cycle.
Two SPUs share an ARM host via AXI bus, operating independently or cooperatively.
Each SPU includes 256 KB instruction/data memory, general/special-purpose registers, and programmable neuron–synapse cores.
Supports real-time inference on FPGA under low-power and moderate resource conditions.
Custom ISA for Spike Computation
Dedicated spike-vector instructions accelerate spike convolution and self-attention.
Supports 8/16/32-bit SIMD accumulators and composite instructions for bitwise AND + popcount + accumulation in one cycle.
Fully synthesizable and low-latency, ideal for neuromorphic workloads.
Efficient Event Compression
Built-in Run-Length Encoding (RLE) + Variable-Length Quantity (VLQ) compression reduces data volume by >98%.
Example: 600 KB → 6 KB average (≈92× reduction).
Enables real-time throughput under limited memory/bandwidth.
Programmable Neurons & Synapses
Software-defined neuron and synapse models tightly integrated with SPU.
Supports multiple neuron types: LIF, adaptive LIF, Sigma–Delta, and Hodgkin–Huxley.
Modular synapse framework allows CSNN, feed-forward, and spike-transformer architectures.
Example configuration: 678 neurons, 70,621 synapses, stored efficiently in compressed tables.
Model & Quantization Support
Fully connected LIF-based SNNs implemented for MNIST, N-MNIST, and ADFTD (EEG) datasets.
INT8 quantization with fixed scale factors for on-chip compatibility.
Ternary quantization ({–1, 0, +1}) enables MAC-free computation using bitwise AND + popcount operations — reducing computation and power.
EXPERIMENTS & RESULTS
All MindCore components were implemented in fully synthesizable RTL and deployed on a Xilinx ZCU104 FPGA for real-time validation.
The system achieved timing closure at 100 MHz, confirming functional stability, low resource utilization, and outstanding energy efficiency compared with GPU baselines.
FPGA Prototyping
Platform: Xilinx ZCU104 (Zynq UltraScale+ MPSoC)
Dual Spiking Processing Units (SPUs) integrated via AXI interconnects.
Utilization: 9 % LUTs, 4 % Registers, 82 % BRAM, 0.5 % DSPs.
Power: Active = 1.9 W / Idle = 1.8 W → extremely low dynamic power.
Clock: 100 MHz (no manual placement required).
Confirmed cycle-accurate RTL vs. simulation behavior.
Software Toolchain
Complete Python–C/C++ toolchain supports model compilation, scheduling, and runtime control.
Converts PyTorch/CuPy SNNs into MindCore-compatible binaries.
Implements instruction scheduling, binary transfer, DMA-based data streaming, and live spike monitoring.
Host API allows control of neuron parameters, thresholds, and timing windows from the ARM core.
Dataset and Training Setup
Datasets: MNIST, N-MNIST (event-based), ADFTD (EEG).
Preprocessing:
N-MNIST → MaxPool (32×32 → 17×17) + compression.
MNIST → Poisson encoding (100 timesteps).
ADFTD → Normalized EEG channels (19).
Training: 100 epochs on RTX A5000 GPU → quantized (INT8 / ternary).
Hyperparameters: τ = 2, vₜₕ = 1, v_reset = 0.
Applications & Future Work
The implemented MindCore architecture will be extended to support spike-driven Transformer models for vision applications, enabling high performance with minimal energy consumption.
Future developments will also integrate advanced neuron models such as Sigma–Delta neurons and Adaptive LIF neurons, expanding MindCore’s capability to support EEG-based Alzheimer’s and dementia prediction as well as ECG-based cardiovascular disease detection systems.